## Slide 1: Building Trust in Modern Computing Platforms
Aritra Dhar
ETH Zurich

## Slide 2: Remote safety/security-critical systems
Images are from janztec, wired, getty, controlbyweb
Notes: First I will motivate you with some relevant examples that involves remote safety and security critical systems. Automation in industrial sector is getting more prevalent today and more and more of our critical infrastructure such a the electricity grid, gas pipelines, are monitored and actuated by these PLC or programmable logic controller. Compared to traditional PLCS, these are often web-enabled, i.e., they are networked attached and provide a web UI. The operators can remotely connect to the devices, monitor and actuate the equipments.
Other critical systems such as medical implants such as a pacemaker are becoming more and more smart so that a medical technicians can connect to them and monitor vitals or change some operational parameters. Smart homes are also another example where IoT devices report the current state of the home and user can operate them remotely. They also provide web or mobile enabled UI. Other, more traditional use cases could be financial transaction. And more and more people, specially during pandemic are opting for these web services.

## Slide 3: Remote safety/security-critical systems
Images are from janztec, wired, getty, controlbyweb
Notes: All of these applications have one critical aspect common in them, they all rely on the commodity OS, hypervisors, VMs and browser to interact with the remote systems. And the reliability of these systems are dependent on how the user provide input to them and perceive output.

## Slide 4: Large TCB Large Attack Surface
25.16M
20.92M
2M
36.68M
600K
CPU microcode
Device firmware
Device drivers
Notes: As the most of the enc users rely on the off the shelf software and hardware such as the browsers and OS/ hypervisors. These are complex software and have millions of lines of code. Which also indicates that they have a large attack surface. And remember that this is just the tip of the iceberg, most of the processor microcode, device drivers and firmware are proprietary. E.g., android is open source but most of the code bases are preoperatory SoC firmware .

## Slide 5: Attacks
Images are from wired, csmonitor, heimdalsecurity
Notes: Over the time, we have seen a number of attacks that exploits such vulnerability in the OS, device drivers, device firmware such as routers etc.

## Slide 6: Attacks
Images are from wired, csmonitor, heimdalsecurity
Notes: Safety critical systems such as the industrial controller are also targets of increased attacks due to their large complexity and usage of commodity hardware and software

## Slide 7: Attacks
Images are from wired, csmonitor, heimdalsecurity
Notes: Not only the complexity in the software but complexity in the hardware also opens up a large attack surface as a large number of hardware components are squished into a small space and there is no possible way to verify and sophisticated supply chain attach such as an analog malware

## Slide 8: Attacks
Images are from wired, csmonitor, heimdalsecurity
Notes: BadUSB is also one of the example where a sophisticated supply chain attack can implant malware into the USB and sniff all the sensitive data

## Slide 9: Attacks
Images are from wired, csmonitor, heimdalsecurity
Notes: And of course, one of the most memorable attacks is the wanncry ransomware attack that exploits an outdated network protocol in Windows XP and cripple entire NHS, the British healthcare systems

## Slide 10: Concrete Attack Scenario
Program
Cancel
Heart beat
Insulin (U)
Remote device
Low limit (mg/dL)
High limit (mg/dL)
Basal rate (U/Hr)
75
177
0.025
60
105
Aritra Dhar
65
Notes: The attacker can not only see the input parameter, but also introduce arbitrary modifications into them, resulting in the misconfiguration in these implants that have serious effect.
Compared to wanncry that was a a malware, the next attack could be more stealthy.

## Slide 11: Remote Trusted path
Host
Remote System
IO devices
User
Notes: Trusted path is an umbrella term that denotes the integrity and confidentiality of the channel between the user IO devices and the target TCB, remote trusted path is an extension where all the communication goes over the untrusted local platform and the network that is also attacker controlled.

## Slide 12: Trusted Execution Environment (TEE)
CPU
Operating System
App
App
App
Operating System
App
App
Enclave
Traditional platforms
Intel SGX
TCB
TCB
TCB
OS still manages devices
Static HW TCB
DRAM
Dev
CPU
DRAM
Dev
Notes: Now TEEs sounds like the perfect way one can solve the problem of large TCB presented by the OS and hypervisors.
Trusted Execution Env or TEE solves some of this problem by reducing the TCB. In traditional platforms, the TCB consists of the application, OS and the hardware. Where in TEE, the application or the enclave is isolated from the OS and other apps by security primitives implemented by the micro processor. In intel SGX, hardware components such as the DRAM and external devices can be attacker-controlled, further reducing the TCB.
However, it is still not straightforward to implement a trusted path in the TEE as the OS still manages all the drivers. Remote attestation is also requires trust in first use which makes the enclaves venerable at the very first attestation. I will revisit this topic later in this talk, and also biggest problem is somewhat static hardware TCB which is sometime hard to define. For example Intel SGX need to trust the Intel ME that manages Nvstorage.

## Slide 13: Disaggregated computing
Central executioner coordinator
Images are from nVidia, Dell, Mellanox official websites
Traditional CPU-centric model
Notes: However, tg

## Slide 14: My Contribution
Remote trusted path application
  IntegriKey (2017, eprint: 2017/1245)
  ProtectION (NDSS 2020)
  IntegriScreen (2018, arXiv:2011.13979)
Remote system

## Slide 15: My Contribution
Remote trusted path application
  IntegriKey (2017, eprint: 2017/1245)
  ProtectION (NDSS 2020)
  IntegriScreen (2018, arXiv:2011.13979)
ProximiTEE (CODASPY 2020)
Remote system

## Slide 16: My Contribution
Remote trusted path application
  IntegriKey (2017, eprint: 2017/1245)
  ProtectION (NDSS 2020)
  IntegriScreen (2018, arXiv:2011.13979)
ProximiTEE (CODASPY 2020)
  Dedicated Security Chips in the Age of Secure Enclaves (IEEE S&P magazine 2020)
Remote system

## Slide 17: My Contribution
Remote trusted path application
  IntegriKey (2017, eprint: 2017/1245)
  ProtectION (NDSS 2020)
  IntegriScreen (2018, arXiv:2011.13979)
ProximiTEE (CODASPY 2020)
  Dedicated Security Chips in the Age of Secure Enclaves (IEEE S&P magazine 2020)
  PIE (2020, arXiv:2010.10416)
Remote system

## Slide 18: My Contribution
Remote trusted path application
  IntegriKey (2017, eprint: 2017/1245)
  ProtectION (NDSS 2020)
  IntegriScreen (2018, arXiv:2011.13979)
ProximiTEE (CODASPY 2020)
  Dedicated Security Chips in the Age of Secure Enclaves (IEEE S&P magazine 2020)
  PIE (2020, arXiv:2010.10416)
Remote system

## Slide 19: Today’s Talk
Remote trusted path application
  IntegriKey (2017, eprint: 2017/1245)
  ProtectION (NDSS 2020)
  IntegriScreen (2018, arXiv:2011.13979)
ProximiTEE (CODASPY 2020)
  Dedicated Security Chips in the Age of Secure Enclaves (IEEE S&P magazine 2020)
  PIE (2020, arXiv:2010.10416)
Remote system
Notes: However I will also revisit some of the works

## Slide 20: ProtectIOn setting
Remote trusted path application
Remote system

## Slide 21: Solution 1: Transaction Confirmation Device
Program
Cancel
Heart beat
Insulin (U)
Remote device
Low limit (mg/dL)
High limit (mg/dL)
Basal rate (U/Hr)
75
177
0.025
60
105
Android Protected Confirmation
You are going to program
Heart beat 75
Insulin 177U
Basal rate 0.025 U/Hr
Low level 60 mg/dL
High level 105 mg/dL
And more ……
Notes: Good for binary decisions, but not for complex large UI

## Slide 22: Solution 2: Input Signing
Trusted embedded device
Program
Cancel
Heart beat
Insulin (U)
Remote device
Low limit (mg/dL)
High limit (mg/dL)
Basal rate (U/Hr)
75
177
0.025
60
105
Heart beat 75
Insulin 177U
Basal rate 0.025 U/Hr
Low level 60 mg/dL
High level 105 mg/dL
Notes: We started to explore this concept with Integrikey …

## Slide 23: Display manipulation attack
17
177
177
177
7
1777
User sees 177
Device records 1777
Host sends 1777
Insulin
Insulin
Notes: Mention that this is not just an implementation issue but more of a fundamental design problem.

## Slide 24: Observation 1
The lack of output integrity – the render of user inputs on the screen – compromises input integrity.

## Slide 25: Solution 3: Overlay
Program
Cancel
Heart beat
Insulin (U)
Remote device
Low limit (mg/dL)
High limit (mg/dL)
Basal rate (U/Hr)
75
177
0.025
60
105
Program
Cancel
Heart beat
Insulin (U)
Remote device
Low limit (mg/dL)
High limit (mg/dL)
Basal rate (U/Hr)

## Slide 26: Overlay: Output Manipulation
Program
Cancel
Heart beat
Insulin (U)
Remote device
Low limit (mg/dL)
High limit (mg/dL)
Basal rate (U/Hr)
Program
Cancel
Insulin (U)
Heart rate
Remote device
Low limit (mg/cc)
High limit (mg/cc)
Basal rate (U/Hr)

## Slide 27: Overlay: Output Manipulation
Program
Cancel
Insulin (U)
Heart rate
Remote device
Low limit (mg/cc)
High limit (mg/cc)
Basal rate (U/Hr)
75
177
0.025
6000
10500
Program
Cancel
75
Heart rate
177
Insulin (U)
Remote device
Low limit (mg/dL)
High limit (mg/dL)
0.025
Basal rate (U/Hr)
60
105

## Slide 28: Observation 2
If the protected output is provided out-of-context, users are more likely not to verify it.
Therefore input integrity can be violated.

## Slide 29: Overlay: Early Form Submission Attack
Textbox in focus
Program
Cancel
Heart beat
Insulin (U)
Remote device
Low limit (mg/dL)
High limit (mg/dL)
Basal rate (U/Hr)
75
17
0.025
60
105
OS triggers click
Fidelius
Trusted overlay from FPGA

## Slide 30: Observation 3
If not all the modalities of inputs are secured simultaneously,
none of them can be fully secured.
Notes: From these observations, we can derive a set of requirements that are fundamental for the security of a remote trausted path

## Slide 31: Requirements
Inter-dependency between Input and output
The lack of output integrity – the render of user inputs on the screen – compromises input integrity.

## Slide 32: Requirements
All modalities of input
If not all the modalities of inputs are secured simultaneously, none of them can be fully secured.

## Slide 33: Requirements
Low cognitive load
If the protected output is provided out-of-context, users are more likely not to verify it. Therefore input integrity can be violated.

## Slide 34: Requirements
Low TCB and easy deploy

## Slide 35: Requirements

## Slide 36: ProtectIOn
Input modalities
Low TCB + fast deployment
IOHub

## Slide 37: IO Integrity – Overlay Generation
Program
Cancel
Insulin (U)
Heart rate
Remote device
Low limit (mg/cc)
High limit (mg/cc)
Basal rate (U/Hr)
<form action=“/some_action”, signature = “0x45AB…”, id = “0x0ab”>
Simultaneous IO
<label for=“insulin” secure=“true”>Insulin</label> <input type="text" id=“insulin" name=“insulin” secure=“true”>

## Slide 38: IO Integrity – Overlay Generation
Simultaneous IO

## Slide 39: IO Integrity – Overlay Generation
Program
Cancel
Insulin (U)
Heart rate
Remote device
Low limit (mg/cc)
High limit (mg/cc)
Basal rate (U/Hr)
Verified UI from secure_site.io
Simultaneous IO

## Slide 40: IO Integrity – Input
Program
Cancel
Insulin (U)
Heart rate
Remote device
Low limit (mg/cc)
High limit (mg/cc)
Basal rate (U/Hr)
Verified UI from secure_site.io
75
177
0.025
60
105
Simultaneous IO

## Slide 41: Grabbing User Attention
Output Integrity: Low cognitive load
Several existing mechanisms
Put 1 in front of all inputs
Low cognitive load

## Slide 42: Grabbing User Attention
Put 1 in front of all inputs
Low cognitive load
Output Integrity: Low cognitive load
Several existing mechanisms
  Lightbox

## Slide 43: Grabbing User Attention
Output Integrity: Low cognitive load
Several existing mechanisms
  Lightbox
  Highlight
Low cognitive load
Put 1 in front of all inputs

## Slide 44: Grabbing User Attention
Output Integrity: Low cognitive load
Several existing mechanisms
  Lightbox
  Highlight
  Freezing
Put 1 in front of all inputs
Low cognitive load

## Slide 45: Grabbing User Attention
Put 1 in front of all inputs
Output Integrity: Low cognitive load
Several existing mechanisms
  Lightbox
  Highlight
  Freezing
  Combination
Low cognitive load

## Slide 46: Grabbing User Attention
Output Integrity: Low cognitive load
Several existing mechanisms
  Lightbox
  Highlight
  Freezing
  Combination
How to determine when to engage?
  Track pointer
  Mouse movement on the overlay
Low cognitive load

## Slide 47: Prototype and TCB
25.16M
20.92M
2M
71K
600K
36.68M
1.9K
3.5K
893
121K
Low TCB
Fast deployment
Notes: Apart from the low TCB, IOHUB also have limited interfaces that are hard to exploit. HDMI is one way and the USB interfaces only have relay operation, this significantly limits the attacker’s ability to find an exploit.

## Slide 48: Performance
Display latency: 21.67 ms
  ~46 fps
Mouse latency: 250
Keyboard latency: 170
Pointer detection accuracy: 0.997

## Slide 49: ProtectIOn ProximiTEE
Remote trusted path application

## Slide 50: ProtectIOn ProximiTEE
Remote trusted path application
Identity of the platform

## Slide 51: Motivation: Remote Attestation
Challenge
CPU
Enclave
Verifier
Report
Signed report
A legitimate platform
A legitimate enclave
Sensitive data
Platform PK
Notes: Assume the enclave is accessing your sensitive medical data. As an user you want to know if you are actually executing the actual enclave coming from a reputed software developer or the attacker is impersonating as the legitimate software and may steal your data. To protect against this, TEEs provide remote attestation that enables the user to verify the software….
The processor has an embedded key that is burned into the fuses during the manufacturing process. The key proves that it is a legitimate intel processor.
The attestation report not only contain the code, stack and heap, but also the micro code version number to make sure that attesting platform is using the updated version of the CPU microcode.
After attestation the verifier asserts that 1) she is communicating with a legitimate intel platform and 2) the enclave code is legitimate -- EPID
Problem: a platform, not a specific one

## Slide 52: Relay Attacker
CPU
OS
Verifier
Enclave
App
CPU
OS
Enclave
App
Challenge
Relay challenge
Signed report
Signed report
Assign secret
Target platform
Attacker’s platform
Notes: Relay attacker, Platforms could be geographically separated. Verifier still gets the proper output – a platform and a legitimate enclave. She attest the attacker’s platform rather that the target platform.
** The attack is possible due to the trust on first use property in SGX remote attestation. Note that this problem is not only limited to the SGX but most of the TEEs that provide remote attestation. All the flavors of remote attestation are vulnerable to the relay attack. This include EPID, pseudonymous and other PKI based remote attestation.
** Implication if the relay attack – mention plunder volt.

## Slide 53: Our Contribution: Auxiliary Device
Verifier
Target platform
Attacker’s platform
CPU
OS
Enclave
App
CPU
OS
Enclave
App
ProximiKey
Notes: The main idea here is to distinguish a relay attack from a physical connection. On a high level, we can reduce this problem to a distance bounding problem that is common in wireless communication. Here we can see how we can port the distance bounding protocol to TEEs.

## Slide 54: ProximiTEE
Verifier
Target platform
Attacker’s platform
CPU
OS
Enclave
App
CPU
OS
Enclave
App
Establish secure channel
ProximiKey

## Slide 55: ProximiTEE
Target platform
CPU
OS
Enclave
App
ProximiKey

## Slide 56: ProximiTEE
Target platform
CPU
OS
Enclave
App
ProximiKey
Initiate remote attestation
Report + platform pk

## Slide 57: ProximiTEE
Target platform
CPU
OS
Enclave
App
ProximiKey
Secure channel

## Slide 58: ProximiTEE
Target platform
CPU
OS
Enclave
App
ProximiKey
Challenge
Response
Calculate latency
Determine proximity

## Slide 59: ProximiTEE
Target platform
CPU
OS
Enclave
App
ProximiKey
Attacker’s platform
CPU
OS
Enclave
App
Verifier

## Slide 60: ProximiTEE
Verifier
Target platform
CPU
OS
Enclave
App
Attacker’s platform
CPU
OS
Enclave
App
Latency > threshold
Possible relay attack

## Slide 61: ProximiTEE
Verifier
Target platform
CPU
OS
Enclave
App
Attacker’s platform
CPU
OS
Enclave
App
Signed report
Signed proximity result
A specific legitimate platform
A legitimate enclave running on that platform

## Slide 62: Setup: Simulating a Powerful Attacker
ProximiKey
Target platform
Attacker’s platform
1m Ethernet cable
USB 3.0 interface
Instant computation
Co-located attacker
ProximiKey based on Cypress EZ-USB FX3

## Slide 63: Main Experimental Result
Local USB: Spans: , average:
Ethernet: Spans: , average:
Samples ( normal traces and simulated attack traces)
Multiple rounds

## Slide 64: Proximity Verification Result
Robust:
Secure: for 50 rounds
Notes: Red and blue are two different readings … attacker’s success probabilty goes down

## Slide 65: Potential Use case: Trusted IO with Enclaves in Data Centre
User’s PC
Data center
I/O
I/O
User

## Slide 66: Potential Use case: Setup of Permissioned Blockchain
Authority
Consensus node
Consensus node
Consensus node
Verifiers
Verifiers

## Slide 67: ProtectIOn ProximiTEE PIE
Remote trusted path application
Identity of the platform

## Slide 68: ProtectIOn ProximiTEE PIE
Remote trusted path application

## Slide 69: Challenges
Secure communication
Remote attestation
Runtime attacks
Notes: In the disaggregation model, we need to address a number of challenges, the first being the secure communication. As the execution is now distributed over multiple hardware components, we need to make sure that the communication between these components and the CPU cores are protected.

## Slide 70: Challenges
Secure communication
Remote attestation
Runtime attacks
Notes: In traditional TEEs, the remote attestation is only limited to the enclaves that re running on the CPU cores. However, if we assume that the execution environments are distributed over multiple hardware component, this needs to be adopted.

## Slide 71: Challenges
Secure communication
Remote attestation
Runtime attacks

## Slide 72: Challenges
Secure communication
Remote attestation
Runtime attacks
Notes: Secure communication is a challenge between one need to secure the communication between the CPU core enclaves and the peripheral firmware

## Slide 73: Can Existing TEEs Solve this Problem?
Secure world & non-secure world
ARM TrustZone
OS
CPU
Peripheral
App
App
Enclave
Intel SGX
M-mode
S-mode
U-mode
OS
Security Monitor
App
App
Enclave
RT
S-ROT
Peripheral
RISC-V KeyStone
Can Existing TEEs Solve this Problem?
Sanctuary
VButton
SGXIO
Graviton (SGX + nVidia GPU)
CURE
Notes: TrustZone mention that there is no isolation between the secure world applications. TrustZone requires to trust entire SoC so no flexible HW TCB
SGX and keystone rely on the OS the relay the communication to the external HW and they also does not provide any flexible TEE + execution happing outside the CPU
Some of the work like Graviton do talk about enclaves on GPU but its very specific only to the GPU and does not extend to general devices, SGXIO need to trust a hypervisor which is a step back

## Slide 74: Challenges are needed to be adapted
Secure communication
Remote attestation
Runtime attacks
Notes: In such a disaggregated model,

## Slide 75: Challenges are needed to be adapted
Secure communication
Remote attestation
Runtime attacks
TCB
Least privilege

## Slide 76: PIE: Platform Isolation Environment
Platform-wide enclave
Application
Driver
Device
Application enclave
Controller enclave
Device
Traditional software model:
PIE software model:

## Slide 77: Communication in Platform Wide enclave
Shared memory
0x00
0x0FF
Firmware enclave
Controller enclave
Application enclave
EPC
EPC
Shared
Shared
HW-backed isolation
PMP entries:

## Slide 78: Platform-awareness
Connect
EPC
EPC
EPC
EPC
Shared
Disconnect
Shared
EPC
EPC
Destroy internal states
Reset
OS
Security Monitor
App
App
Enclave
RT
S-ROT
Peripheral

## Slide 79: Platform-wide Attestation
DMA params
DMA params
AC policies
AC policies
Application enclave report
Controller enclave 1 report
Controller enclave 2 report
report
report

## Slide 80: Platform-wide Attestation
DMA params
DMA params
AC policies
AC policies
Application enclave report
Controller enclave 1 report
Controller enclave 2 report
report
report
Application enclave 2 report
DMA params

## Slide 81: Summary of the properties
Platform-wide enclaves
Shared memory communication
Platform awareness
Platform-wide attestation

## Slide 82: Prototype: simple IO peripherals
Peripheral emulation
PMOD peripheral
FPGA running application class RISC-V core with PMP
over GPIO
2.5 KLoC peripheral code
50 LoC for driver
Attestation 60

## Slide 83: Prototype: Accelerator
Multi-tenant isolation
4096-core RISC-V* accelerator based on Snitch**
Addition of PMP
  Small increase in the core size
  750 MHz with 0 PMP
  666 MHz with 4 PMP
* Florian Zaruba et. al. 2020. A 4096-core RISC-VChiplet Architecture for Ultra-efficient Floating-point Computing. In2020 IEEEHot Chips 32 Symposium (HCS). IEEE Computer Society, 1–24.
** F. Zaruba et. al. 2020.Snitch: A tinyPseudo Dual-Issue Processor for Area and Energy Efficient Executionof Floating-Point Intensive Workloads.IEEE Trans. Comput.(2020)

## Slide 84: Context switch performance

## Slide 85: Summary
Remote trusted path application
Remote system
ProximiTEE
PIE
ProtectIOn
Notes: However I will also revisit some of the works

## Slide 86
Thank you! Questions?

## Slide 87: Other contributions
Fast off-chain payments
  Snappy (NDSS 2020)
Anonymous communication
  CoverUp (NSDI 2019)
Monitoring of type-state properties
  Metis (RV 2018)
Rollback protection for SGX
  ROTE (USENIX 2017)

## Slide 88: Secure Communication
SM
RT+E
OS
Shared
OS
SM
App
App
Enclave
RT
Pmp0
Pmp1
Pmp2
000
000
111
Pmp2
111

## Slide 89: Secure Communication
SM
RT+E
OS
Shared
OS
SM
App
App
Enclave
RT
Pmp0
Pmp1
Pmp2
000
000
111
Pmp2
111
RISC-V PMP

## Slide 90: Secure Communication
SM
RT+E
OS
Shared
OS
SM
App
App
Enclave
RT
Pmp0
Pmp1
Pmp2
000
111
000
Pmp2
111
RISC-V PMP

## Slide 91: Secure Communication
SM
RT+E
OS
Shared
OS
SM
App
App
Enclave
RT
Pmp0
Pmp1
Pmp2
000
111
000
Pmp2
111
RISC-V PMP

## Slide 92: Secure Communication
SM
RT+E
OS
Shared
OS
SM
App
App
Enclave
RT
Pmp0
Pmp1
Pmp2
000
111
000
Pmp2
111
RISC-V PMP: Physical Memory Protection

## Slide 93: Secure Communication
SM
RT+E
OS
Shared
OS
SM
App
App
Enclave
RT
Pmp0
Pmp1
Pmp2
000
000
111
Pmp2
111
RISC-V PMP
Use PMP entries for shared buffers

## Slide 94: Traditional CPU-centric Model
Security Monitor (SM)
USB
PCI
Memory
Processor
SATA
TB
Notes: But the biggest problem that TEE have is that they are focus towards traditional computation model where all the computation is executed on the application running on the CPU core. The CPU also manages other peripherals and communicate them over shared memory or memory mapped IO.

## Slide 95: Secure Communication
RISC-V PMP: Physical Memory Protection
SM
RT+E
OS
Shared
OS
Pmp0
Pmp1
Pmp2
000
000
111
Pmp2
000

## Slide 96: Platform-wide Attestation
Controller enclave 1
Controller enclave 2
Connect
Connect
Send Cert
Send Cert

## Slide 97: Platform-wide Attestation
Application enclave
Controller enclave 1
Controller enclave 2
Connect
Connect

## Slide 98: Platform-wide Attestation
Application enclave
Controller enclave 1
Controller enclave 2
Connect
Connect

## Slide 99: Platform-wide Attestation
Application enclave
Controller enclave 1
Controller enclave 2
Challenge

## Slide 100: Platform-wide Attestation
Application enclave
Controller enclave 1
Controller enclave 2
App enclave report
Controller enclave 1 ID
Controller enclave 2 ID

## Slide 101: Platform-wide Attestation
Application enclave
Controller enclave 1
Controller enclave 2
App enclave report
Controller enclave 1 ID
Controller enclave 2 ID

## Slide 102: Platform-wide Attestation
Application enclave
Controller enclave 1
Controller enclave 2
Challenge
Challenge

## Slide 103: Platform-wide Attestation
Application enclave
Controller enclave 1
Controller enclave 2
Controller enclave 1 report + report
Controller enclave 2 report + report

## Slide 104: Platform-wide Attestation
Firmware report
AE report +
CE list
Connect
Firmware
Controller enclave
Application enclave
Connect
Remote verifier
Challenge
Deploy
Establish shared memory
Establish shared memory
Shared memory comm
Shared memory comm
Remote attestation
CE + firmware report
Secret
provision
Includes connection parameters

## Slide 105: Summary
ProtectIOn
  Observation of existing trusted path systems
  Fundamental security properties
  A system that encapsulates all these properties
ProximiTEE
  Porting trusted path solution in TEEs is non-trivial
  Trust on First use in remote attestation: rerouting attack
  Distance bounding to identify a platform
PIE
  Disaggregate compute model
  Platform-wide enclaves: extend enclaves from CPU cores to other HW
  Platform awareness and platform-wide attestation