## Slide 1: Building Trust in Modern Computing Platforms
Aritra Dhar
ETH Zurich
Notes: Thanks for the introduction. And thanks for attending my talk. I am Aritra, Ph.D. student from ETH Zurich, and I am going to talk about a part of my doctoral thesis today which is about how to bring trust in modern computing platforms.

## Slide 2: Remote safety/security-critical systems
Images are from janztec, wired, getty, controlbyweb
Notes: First I will motivate you with some relevant examples that involves remote safety and security critical systems. Automation in industrial sector is getting more prevalent today and more and more of our critical infrastructure such a the electricity grid, gas pipelines, are monitored and actuated by these PLC or programmable logic controller. Compared to traditional PLCS, these are often web-enabled, i.e., they are networked attached and provide a web UI to access them. Other critical systems such as medical implants such as a pacemaker are becoming more and more smart so that a medical technicians can connect to them and monitor vitals or change some operational parameters. Smart homes are also another example where IoT devices report the current state of the home and one can actuate components. They also provide web or mobile enabled UI. Other, more traditional use cases could be financial transaction. The most common are banking, however cryptocurrency is on the rise and unlike a brick and mortar bank, they rely on the web services.

## Slide 3: Remote safety/security-critical systems
Images are from janztec, wired, getty, controlbyweb
Notes: All of they enable users to use their platform which are off the shelf computers to access their browser to access these services. Here is one of the example with the web enabled PLC made by controlby web. That provide rich UI interfaces that not only provide a many different way to input to the system but to interpret the output. And these are very critical for the proper operation of these devices.

## Slide 4: Large Attack Surface
25.16M
20.92M
2M
71K
600K
36.68M
CPU microcode
Device firmware
Device drivers
….
Notes: As the most of the enc users rely on the off the shelf software and hardware such as the browsers and OS/ hypervisors. These are complex software and have millions of lines of code. Which also indicates that they have a large attack surface. And remember that this is just the tip of the iceberg, most of the processor microcode, device drivers and firmware are proprietary. E.g., android is open source but most of the code bases are preoperatory SoC firmware .

## Slide 5: Attacks
Images are from wired, csmonitor, heimdalsecurity
Notes: Over the time, we have seen a number of attacks that exploits such vulnerability in the OS, device drivers, device firmware such as routers etc.

## Slide 6: Attacks
Images are from wired, csmonitor, heimdalsecurity
Notes: Safety critical systems such as the industrial controller are also targets of increased attacks due to their large complexity and usage of commodity hardware and software

## Slide 7: Attacks
Images are from wired, csmonitor, heimdalsecurity
Notes: Not only the complexity in the software but complexity in the hardware also opens up a large attack surface as a large number of hardware components are squished into a small space and there is no possible way to verify and sophisticated supply chain attach such as an analog malware

## Slide 8: Attacks
Images are from wired, csmonitor, heimdalsecurity
Notes: BadUSB is also one of the example where a sophisticated supply chain attack can implant malware into the USB and sniff all the sensitive data

## Slide 9: Attacks
Images are from wired, csmonitor, heimdalsecurity
Notes: And of course, one of the most memorable attacks is the wanncry ransomeare attack that exploits an outdated network protocol in Windows XP and cripple entire NHS, the British healthcare systems

## Slide 10: Concrete Attack Scenario
Program
Cancel
Heart beat
Insulin (U)
Remote device
Low limit (mg/dL)
High limit (mg/dL)
Basal rate (U/Hr)
75
177
0.025
60
105
Aritra Dhar
Notes: Now, we as security researchers are well aware of the complexity of software systems and the attack surface they open up. However, oftentimes, its not clear how these attacks can affect our data to day lives. I will now provide one such concrete attack scenario that focuses on network-controlled medical implants. Two such examples are pacemakers and insulin pumps where the doctor can change vital parameters.

## Slide 11: Concrete Attack Scenario
Program
Cancel
Heart beat
Insulin (U)
Remote device
Low limit (mg/dL)
High limit (mg/dL)
Basal rate (U/Hr)
75
177
0.025
60
105
Aritra Dhar
Notes: The attacker who compromises the entire software stack, i.e., the OS, VM, browser can …

## Slide 12: Concrete Attack Scenario
Program
Cancel
Heart beat
Insulin (U)
Remote device
Low limit (mg/dL)
High limit (mg/dL)
Basal rate (U/Hr)
75
177
0.025
60
105
Aritra Dhar
65
Notes: The attacker can not only see the input parameter, but also introduce arbitrary modifications into them, resulting in the misconfiguration in these implants that have serious on

## Slide 13: Remote Trusted path
Host
Remote server
IO devices
User
Notes: Trusted path is an umbrella term that denotes the integrity and confidentiality of the channel between the user IO devices and the target TCB, remote trusted path is an extension where all the communication goes over the untrusted local platform and the network.

## Slide 14: Trusted Execution Environment (TEE)
CPU
Operating System
App
App
App
Operating System
App
App
Enclave
Traditional platforms
Intel SGX
TCB
TCB
TCB
OS still manages devices
Trust on first use for remote attestation
Static HW TCB
DRAM
Dev
CPU
DRAM
Dev
Notes: Trusted Execution Env or TEE solves some of this problem by reducing the TCB. In traditional platforms, the TCB consists of the application, OS and the hardware. Where in TEE, the application or the enclave is isolated from the OS and other apps by security primitives implemented by the micro processor.

## Slide 15: Traditional CPU-centric Model
Security Monitor (SM)
USB
PCI
Memory
Processor
SATA
TB

## Slide 16: Disaggregated computing
Central executioner coordinator
Images are from nVidia, Dell, Mellanox official websites

## Slide 17: Thesis Contribution
Remote trusted path application
  IntegriKey (2017, eprint: 2017/1245)
  ProtectION (NDSS 2020)
  IntegriScreen (2018, arXiv:2011.13979)

## Slide 18: Thesis Contribution
Remote trusted path application
  IntegriKey (2017, eprint: 2017/1245)
  ProtectION (NDSS 2020)
  IntegriScreen (2018, arXiv:2011.13979)
ProximiTEE (CODASPY 2020)

## Slide 19: Thesis Contribution
Remote trusted path application
  IntegriKey (2017, eprint: 2017/1245)
  ProtectION (NDSS 2020)
  IntegriScreen (2018, arXiv:2011.13979)
ProximiTEE (CODASPY 2020)
  Dedicated Security Chips in the Age of Secure Enclaves (IEEE S&P magazine 2020)

## Slide 20: Thesis Contribution
Remote trusted path application
  IntegriKey (2017, eprint: 2017/1245)
  ProtectION (NDSS 2020)
  IntegriScreen (2018, arXiv:2011.13979)
ProximiTEE (CODASPY 2020)
  Dedicated Security Chips in the Age of Secure Enclaves (IEEE S&P magazine 2020)
Peripheral deriver
  PIE (2020, arXiv:2010.10416)

## Slide 21: Thesis Contribution
Remote trusted path application
  IntegriKey (2017, eprint: 2017/1245)
  ProtectION (NDSS 2020)
  IntegriScreen (2018, arXiv:2011.13979)
ProximiTEE (CODASPY 2020)
  Dedicated Security Chips in the Age of Secure Enclaves (IEEE S&P magazine 2020)
Peripheral deriver
  PIE (2020, arXiv:2010.10416)

## Slide 22: Thesis contribution
Ad-Hoc trusted path solutions
  IntegriKey (2017, eprint: 2017/1245)
  IntegriScreen (2018, arXiv:2011.13979)
Fundamentals of trusted path
  ProtectIOn (NDSS 2020)
Assertion on identity of a platform
  ProximiTEE (CODASPY 2020)
External security chips for TEEs
  Hardware assisted security (IEEE Security & Privacy 2020)
Reconfigurable HW/SW TCB
  PIE (2020, arXiv:2010.10416)
Aritra Dhar

## Slide 23: Other contributions
Fast off-chain payments
  Snappy (NDSS 2020)
Anonymous communication
  CoverUp (NSDI 2019)
Monitoring of type-state properties
  Metis (RV 2018)
Rollback protection for SGX
  ROTE (USENIX 2017)

## Slide 24: Today’s talk
Ad-Hoc trusted path solutions
  IntegriKey (2017, eprint: 2017/1245)
  IntegriScreen (2018, arXiv:2011.13979)
Fundamentals of trusted path
  ProtectIOn (NDSS 2020)
Establishing identity of a platform
  ProximiTEE (CODASPY 2020)
External security chips for TEEs
  Hardware assisted security (IEEE Security & Privacy 2020)
Reconfigurable HW/SW TCB
  PIE (2020, arXiv:2010.10416)
Aritra Dhar

## Slide 25: Today’s talk
Ad-Hoc trusted path solutions
  IntegriKey (2017, eprint: 2017/1245)
  IntegriScreen (2018, arXiv:2011.13979)
Fundamentals of trusted path
  ProtectIOn (NDSS 2020)
Establishing identity of a platform
  ProximiTEE (CODASPY 2020)
External security chips for TEEs
  Hardware assisted security (IEEE Security & Privacy 2020)
Reconfigurable HW/SW TCB
  PIE (2020, arXiv:2010.10416)

## Slide 26: Today’s Talk
Remote trusted path application
  IntegriKey (2017, eprint: 2017/1245)
  ProtectION (NDSS 2020)
  IntegriScreen (2018, arXiv:2011.13979)
ProximiTEE (CODASPY 2020)
  Dedicated Security Chips in the Age of Secure Enclaves (IEEE S&P magazine 2020)
Peripheral deriver
  PIE (2020, arXiv:2010.10416)
Notes: However I will also revisit some of the works

## Slide 27: ProtectIOn setting
Remote trusted path application

## Slide 28: Solution 1: Transaction Confirmation Device
Program
Cancel
Heart beat
Insulin (U)
Remote device
Low limit (mg/dL)
High limit (mg/dL)
Basal rate (U/Hr)
75
177
0.025
60
105
Android Protected Confirmation
You are going to program
Heart beat 75
Insulin 177U
Basal rate 0.025 U/Hr
Low level 60 mg/dL
High level 105 mg/dL
And more ……

## Slide 29: Solution 2: Input Signing
Trusted embedded device
Program
Cancel
Heart beat
Insulin (U)
Remote device
Low limit (mg/dL)
High limit (mg/dL)
Basal rate (U/Hr)
75
177
0.025
60
105
Heart beat 75
Insulin 177U
Basal rate 0.025 U/Hr
Low level 60 mg/dL
High level 105 mg/dL

## Slide 30: Display manipulation attack
17
177
177
177
7
1777
User sees 177
Device records 1777
Host sends 1777
Insulin
Insulin
IntegriKey

## Slide 31: Observation 1
The lack of output integrity – the render of user inputs on the screen – compromises input integrity.

## Slide 32: Solution 3: Overlay
Program
Cancel
Heart beat
Insulin (U)
Remote device
Low limit (mg/dL)
High limit (mg/dL)
Basal rate (U/Hr)
75
177
0.025
60
105
Program
Cancel
Heart beat
Insulin (U)
Remote device
Low limit (mg/dL)
High limit (mg/dL)
Basal rate (U/Hr)

## Slide 33: Overlay: Output Manipulation
Program
Cancel
Heart beat
Insulin (U)
Remote device
Low limit (mg/dL)
High limit (mg/dL)
Basal rate (U/Hr)
Program
Cancel
Insulin (U)
Heart rate
Remote device
Low limit (mg/cc)
High limit (mg/cc)
Basal rate (U/Hr)

## Slide 34: Overlay: Output Manipulation
Program
Cancel
Insulin (U)
Heart rate
Remote device
Low limit (mg/cc)
High limit (mg/cc)
Basal rate (U/Hr)
75
177
0.025
6000
10500

## Slide 35: Observation 2
If the protected output is provided out-of-context,
users are more likely not to verify it.
Therefore input integrity can be violated.

## Slide 36: Overlay: Early Form Submission Attack
Textbox in focus
Program
Cancel
Heart beat
Insulin (U)
Remote device
Low limit (mg/dL)
High limit (mg/dL)
Basal rate (U/Hr)
75
17
0.025
60
105
OS triggers click
Fidelius
Trusted overlay from FPGA

## Slide 37: Observation 3
If not all the modalities of inputs are secured simultaneously, none of them can be fully secured.

## Slide 38: Requirements
Inter-dependency between Input and output
The lack of output integrity – the render of user inputs on the screen – compromises input integrity.

## Slide 39: Requirements
All modalities of input
If not all the modalities of inputs are secured simultaneously, none of them can be fully secured.

## Slide 40: Requirements
Low cognitive load
If the protected output is provided out-of-context, users are more likely not to verify it. Therefore input integrity can be violated.

## Slide 41: Requirements
Low TCB and easy deploy

## Slide 42: Requirements

## Slide 43: ProtectIOn
Input modalities
Low TCB + fast deployment
IOHub

## Slide 44: IO Integrity – Overlay Generation
Program
Cancel
Insulin (U)
Heart rate
Remote device
Low limit (mg/cc)
High limit (mg/cc)
Basal rate (U/Hr)
<form action=“/some_action”, signature = “0x45AB…”, id = “0x0ab”>
Simultaneous IO

## Slide 45: IO Integrity – Overlay Generation
Simultaneous IO

## Slide 46: IO Integrity – Overlay Generation
Program
Cancel
Insulin (U)
Heart rate
Remote device
Low limit (mg/cc)
High limit (mg/cc)
Basal rate (U/Hr)
Verified UI from secure_site.io
Simultaneous IO

## Slide 47: IO Integrity – Input
Program
Cancel
Insulin (U)
Heart rate
Remote device
Low limit (mg/cc)
High limit (mg/cc)
Basal rate (U/Hr)
Verified UI from secure_site.io
75
177
0.025
60
105
Simultaneous IO

## Slide 48: Grabbing User Attention
Output Integrity: Low cognitive load
Several existing mechanisms
Put 1 in front of all inputs
Low cognitive load

## Slide 49: Grabbing User Attention
Put 1 in front of all inputs
Low cognitive load
Output Integrity: Low cognitive load
Several existing mechanisms
  Lightbox

## Slide 50: Grabbing User Attention
Output Integrity: Low cognitive load
Several existing mechanisms
  Lightbox
  Highlight
Low cognitive load
Put 1 in front of all inputs

## Slide 51: Grabbing User Attention
Output Integrity: Low cognitive load
Several existing mechanisms
  Lightbox
  Highlight
  Freezing
Put 1 in front of all inputs
Low cognitive load

## Slide 52: Grabbing User Attention
Put 1 in front of all inputs
Output Integrity: Low cognitive load
Several existing mechanisms
  Lightbox
  Highlight
  Freezing
  Combination
Low cognitive load

## Slide 53: Grabbing User Attention
Output Integrity: Low cognitive load
Several existing mechanisms
  Lightbox
  Highlight
  Freezing
  Combination
How to determine when to engage?
  Track pointer
  Mouse movement on the overlay
Low cognitive load

## Slide 54: Prototype and TCB
25.16M
20.92M
2M
71K
600K
36.68M
1.9K
3.5K
893
121K
Low TCB
Fast deployment

## Slide 55: Performance
Display latency: 21.67 ms
  ~46 fps
Mouse latency: 250
Keyboard latency: 170
Pointer detection accuracy: 0.997

## Slide 56: ProtectIOn ProximiTEE
Remote trusted path application

## Slide 57: ProtectIOn ProximiTEE
Remote trusted path application
Identity of the platform

## Slide 58: Motivation: Remote Attestation
Challenge
CPU
Enclave
Verifier
Report
Signed report
A legitimate platform
A legitimate enclave
Sensitive data
Platform PK
Notes: Assume the enclave is accessing your sensitive medical data. As an user you want to know if you are actually executing the actual enclave coming from a reputed software developer or the attacker is impersonating as the legitimate software and may steal your data. To protect against this, TEEs provide remote attestation that enables the user to verify the software….
The processor has an embedded key that is burned into the fuses during the manufacturing process. The key proves that it is a legitimate intel processor.
The attestation report not only contain the code, stack and heap, but also the micro code version number to make sure that attesting platform is using the updated version of the CPU microcode.
After attestation the verifier asserts that 1) she is communicating with a legitimate intel platform and 2) the enclave code is legitimate -- EPID
Problem: a platform, not a specific one

## Slide 59: Common issue: Relay Attacker
CPU
OS
Verifier
Enclave
App
CPU
OS
Enclave
App
Challenge
Relay challenge
Signed report
Signed report
Assign secret
Target platform
Attacker’s platform
Notes: Relay attacker,
Platforms could be geographically separated.
Verifier still gets the proper output – a platform and a legitimate enclave.
She attest the attacker’s platform rather that the target platform

## Slide 60: Our Contribution: Relay Attack Implications
CPU
OS
Enclave
App
Physical access
Privilege escalation
Undermine platform maintenance
  Defer patch
  Secure target platform
  Insecure attacker’s platform

## Slide 61: Distinguishing is hard
Verifier
Target platform
CPU
OS
Enclave
App
CPU
OS
Enclave
App
Attacker’s platform

## Slide 62: Our Contribution: Auxiliary Device
Verifier
Target platform
Attacker’s platform
CPU
OS
Enclave
App
CPU
OS
Enclave
App
ProximiKey

## Slide 63: ProximiTEE
Verifier
Target platform
Attacker’s platform
CPU
OS
Enclave
App
CPU
OS
Enclave
App
Establish secure channel
ProximiKey

## Slide 64: ProximiTEE
Target platform
CPU
OS
Enclave
App
ProximiKey

## Slide 65: ProximiTEE
Target platform
CPU
OS
Enclave
App
ProximiKey
Initiate remote attestation
Report + platform pk

## Slide 66: ProximiTEE
Target platform
CPU
OS
Enclave
App
ProximiKey
Secure channel

## Slide 67: ProximiTEE
Target platform
CPU
OS
Enclave
App
ProximiKey
Challenge
Response
Calculate latency
Determine proximity

## Slide 68: ProximiTEE
Target platform
CPU
OS
Enclave
App
ProximiKey
Attacker’s platform
CPU
OS
Enclave
App
Verifier

## Slide 69: ProximiTEE
Verifier
Target platform
CPU
OS
Enclave
App
Attacker’s platform
CPU
OS
Enclave
App
Latency > threshold
Possible relay attack

## Slide 70: ProximiTEE
Verifier
Target platform
CPU
OS
Enclave
App
Attacker’s platform
CPU
OS
Enclave
App
Signed report
Signed proximity result
A specific legitimate platform
A legitimate enclave running on that platform

## Slide 71: Simulating a Powerful Attacker
Real-world attack scenario
  Geographically separated
  Multi-hop network
1-meter Ethernet connection
Instant computation
Zero-latency NIC
Ping flood mode
  Fill up the OS network buffer

## Slide 72: Evaluation: Setup
ProximiKey
Target platform
Attacker’s platform
1m Ethernet cable
USB 3.0 interface
Fully implemented
ProximiKey based on Cypress EZ-USB FX3
ProximiTEE API
Hotcalls to avoid OCALLs and ECALLs

## Slide 73: Main Experimental Result
Local USB: Spans: , average:
Ethernet: Spans: , average:
Samples ( normal traces and simulated attack traces)
Multiple rounds

## Slide 74: Proximity Verification Result
Robust:
Secure: for 50 rounds
Notes: Red and blue are two different readings … attacker’s success probabilty goes down

## Slide 75: Potential Use case: Trusted IO with Enclaves in Data Centre
User’s PC
Data center
I/O
I/O
User

## Slide 76: Potential Use case: Setup of Permissioned Blockchain
Authority
Consensus node
Consensus node
Consensus node
Verifiers
Verifiers

## Slide 77: ProtectIOn ProximiTEE PIE
Remote trusted path application
Identity of the platform

## Slide 78: ProtectIOn ProximiTEE PIE
Remote trusted path application
Driver

## Slide 79: Challenges
Secure communication
Remote attestation
Runtime attacks

## Slide 80: Challenges
Secure communication
Remote attestation
Runtime attacks

## Slide 81: Challenges
Secure communication
Remote attestation
Runtime attacks

## Slide 82: Challenges
Secure communication
Remote attestation
Runtime attacks
Notes: Secure communication is a challenge between one need to secure the communication between the CPU core enclaves and the peripheral firmware

## Slide 83: Can Existing TEEs Solve this Problem?
Secure world & non-secure world
ARM TrustZone
OS
CPU
Peripheral
App
App
Enclave
Intel SGX
M-mode
S-mode
U-mode
OS
Security Monitor
App
App
Enclave
RT
S-ROT
Peripheral
RISC-V KeyStone
Can Existing TEEs Solve this Problem?
Sanctuary
VButton
SGXIO
Graviton (SGX + nVidia GPU)
CURE
Notes: TrustZone mention that there is no isolation between the secure world applications. TrustZone requires to trust entire SoC so no flexible HW TCB
SGX and keystone rely on the OS the relay the communication to the external HW and they also does not provide any flexible TEE + execution happing outside the CPU
Some of the work like Graviton do talk about enclaves on GPU but its very specific only to the GPU and does not extend to general devices, SGXIO need to trust a hypervisor which is a step back

## Slide 84: Challenges are needed to be adapted
Secure communication
Remote attestation
Runtime attacks

## Slide 85: Challenges are needed to be adapted
Secure communication
Remote attestation
Runtime attacks
TCB
Least privilege

## Slide 86: Attacker model
Type I : Sensors
  Remote attacker
Type II : Compute Devices
  Local physical attacker

## Slide 87: PIE
Platform-wide enclave
Three types of enclave
  Application enclave
  Controller enclave
    Multi app isolation
    Policy enforcement
  Firmware enclave
Communication over shared memory
  Enclave: EPC + shared buffer
0x00
0x0FF
Firmware enclave
Controller enclave
Application enclave

## Slide 88: Secure Communication
SM
RT+E
OS
Shared
OS
SM
App
App
Enclave
RT
Pmp0
Pmp1
Pmp2
000
000
111
Pmp2
111

## Slide 89: Secure Communication
SM
RT+E
OS
Shared
OS
SM
App
App
Enclave
RT
Pmp0
Pmp1
Pmp2
000
000
111
Pmp2
111
RISC-V PMP

## Slide 90: Secure Communication
SM
RT+E
OS
Shared
OS
SM
App
App
Enclave
RT
Pmp0
Pmp1
Pmp2
000
111
000
Pmp2
111
RISC-V PMP

## Slide 91: Secure Communication
SM
RT+E
OS
Shared
OS
SM
App
App
Enclave
RT
Pmp0
Pmp1
Pmp2
000
111
000
Pmp2
111
RISC-V PMP

## Slide 92: Secure Communication
SM
RT+E
OS
Shared
OS
SM
App
App
Enclave
RT
Pmp0
Pmp1
Pmp2
000
111
000
Pmp2
111
RISC-V PMP

## Slide 93: Secure Communication
SM
RT+E
OS
Shared
OS
SM
App
App
Enclave
RT
Pmp0
Pmp1
Pmp2
000
000
111
Pmp2
111
RISC-V PMP
Use PMP entries for shared buffers

## Slide 94: Platform-awareness
Additional enclaves states
  Based on moving ownership
  Connect :
    Device tree by the zero-stage bootloader
  Disconnect :
Two types of disconnect
  Synchronous
  Asynchronous
  Zeros out all the internal states

## Slide 95: Platform-wide Attestation
Firmware report
AE report +
CE list
Attach
Firmware
Controller enclave
Application enclave
Connect
Remote verifier
Challenge
Deploy
Establish shared memory
Establish shared memory
Shared memory comm
Shared memory comm
Remote attestation
CE + firmware report
Secret
provision
Includes connection parameters

## Slide 96: Summary of the properties
Platform-wide enclaves
  Abstraction layer on enclaves
  Distributed over CPU cores, external hardware …
Shared memory communication
  Tighter control over interaction
  PMP ensures isolation
Platform awareness
  Lifecycle events: adapt with flexible hardware
Platform-wide attestation
  Measurement + communication parameters
  Least privilege on hardware TCB only trust what you use (attest)

## Slide 97: Prototype: simple IO peripherals
Peripheral emulation
PMOD peripheral
FPGA running application class RISC-V core with PMP

## Slide 98: Prototype: Accelerator
Multi-tenant isolation
4096-core RISC-V* accelerator based on Snitch**
Addition of PMP
  Small increase in the core size
  750 MHz with 0 PMP
  666 MHz with 4 PMP
* Florian Zaruba, Fabian Schuiki, and Luca Benini. 2020. A 4096-core RISC-VChiplet Architecture for Ultra-efficient Floating-point Computing. In2020 IEEEHot Chips 32 Symposium (HCS). IEEE Computer Society, 1–24.
** F. Zaruba, F. Schuiki, T. Hoefler, and L. Benini. 2020.Snitch: A tinyPseudo Dual-Issue Processor for Area and Energy Efficient Executionof Floating-Point Intensive Workloads.IEEE Trans. Comput.(2020)

## Slide 99: Context switch performance

## Slide 100: Summary
ProtectIOn
  Observation of existing trusted path systems
  Fundamental security properties
  A system that encapsulates all these properties
ProximiTEE
  Porting trusted path solution in TEEs is non-trivial
  Trust on First use in remote attestation: rerouting attack
  Distance bounding to identify a platform
PIE
  Disaggregate compute model
  Platform-wide enclaves: extend enclaves from CPU cores to other HW
  Platform awareness and platform-wide attestation

## Slide 101
Thank you! Questions?