## Slide 1: Building Trust in Modern Computing Platforms
Aritra Dhar
ETH Zurich

## Slide 2: Remote safety/security-critical systems
Images are from janztec, wired, getty, controlbyweb
Notes: First I will motivate you with some relevant examples that involves remote safety and security critical systems. Automation in industrial sector is getting more prevalent today and more and more of our critical infrastructure such a the electricity grid, gas pipelines, are monitored and actuated by these PLC or programmable logic controller. Compared to traditional PLCS, these are often web-enabled, i.e., they are networked attached and provide a web UI. The operators can remotely connect to the devices, monitor and actuate the equipments.
Other critical systems such as medical implants such as a pacemaker are becoming more and more smart so that a medical technicians can connect to them and monitor vitals or change some operational parameters. Smart homes are also another example where IoT devices report the current state of the home and user can operate them remotely. They also provide web or mobile enabled UI. Other, more traditional use cases could be financial transaction. And more and more people, specially during pandemic are opting for these web services.

## Slide 3: Remote safety/security-critical systems
Images are from janztec, wired, getty, controlbyweb

## Slide 4: Large TCB Large Attack Surface
25.16M
20.92M
2M
36.68M
600K
CPU microcode
Device firmware
Device drivers

## Slide 5: Concrete Attack Scenario
Program
Cancel
Heart beat
Insulin (U)
Program remote device
Low limit (mg/dL)
High limit (mg/dL)
Basal rate (U/Hr)
75
177
0.025
60
105
Aritra Dhar
65

## Slide 6: Remote Trusted path for IO
Host
Remote System
IO devices
User

## Slide 7: Trusted Execution Environment (TEE)
CPU
Operating System
App
App
App
Operating System
App
App
Enclave
Traditional platforms
Intel SGX
TCB
TCB
TCB
OS still manages devices
Static HW TCB
Trusted path is challenging
DRAM
Dev
CPU
DRAM
Dev

## Slide 8: Disaggregated computing
Central executioner coordinator
Images are from nVidia, Dell, Mellanox official websites
Traditional CPU-centric model

## Slide 9: My Contribution
Remote trusted path application
  IntegriKey (2017, eprint: 2017/1245)
  ProtectION (NDSS 2020)
  IntegriScreen (2018, arXiv:2011.13979)
Remote system
Notes: In the beginning of the my doctoral research I started first with IntegriKey and then Integriscreen. The former is based on the idea of input signing to provide only input integrity. Integrikey also identifies a new form of UI attack that we called label swapping attack where the attacker can swap the labels of input element. IntegriScreen provide IO integrity by using a smartphone camera using a concept that we coined visual supervision of user input. While these two works made a substantial progress over state of the art trusted path, we late identify some fundamental pitall not only in them but also almost every existing research….

## Slide 10: My Contribution
Remote trusted path application
  IntegriKey (2017, eprint: 2017/1245)
  ProtectION (NDSS 2020)
  IntegriScreen (2018, arXiv:2011.13979)
ProximiTEE (CODASPY 2020)
Remote system

## Slide 11: My Contribution
Remote trusted path application
  IntegriKey (2017, eprint: 2017/1245)
  ProtectION (NDSS 2020)
  IntegriScreen (2018, arXiv:2011.13979)
ProximiTEE (CODASPY 2020)
  Dedicated Security Chips in the Age of Secure Enclaves (IEEE S&P magazine 2020)
Remote system

## Slide 12: My Contribution
Remote trusted path application
  IntegriKey (2017, eprint: 2017/1245)
  ProtectION (NDSS 2020)
  IntegriScreen (2018, arXiv:2011.13979)
ProximiTEE (CODASPY 2020)
  Dedicated Security Chips in the Age of Secure Enclaves (IEEE S&P magazine 2020)
  PIE (2020, arXiv:2010.10416)
Remote system

## Slide 13: My Contribution
Remote trusted path application
  IntegriKey (2017, eprint: 2017/1245)
  ProtectION (NDSS 2020)
  IntegriScreen (2018, arXiv:2011.13979)
ProximiTEE (CODASPY 2020)
  Dedicated Security Chips in the Age of Secure Enclaves (IEEE S&P magazine 2020)
  PIE (2020, arXiv:2010.10416)
Remote system

## Slide 14: Today’s Talk
Remote trusted path application
  IntegriKey (2017, eprint: 2017/1245)
  ProtectION (NDSS 2020)
  IntegriScreen (2018, arXiv:2011.13979)
ProximiTEE (CODASPY 2020)
  Dedicated Security Chips in the Age of Secure Enclaves (IEEE S&P magazine 2020)
  PIE (2020, arXiv:2010.10416)
Remote system

## Slide 15: ProtectIOn setting
Remote trusted path application
  ProtectION (NDSS 2020)
Remote system

## Slide 16: Solution 1: Transaction Confirmation Device
Program
Cancel
Heart beat
Insulin (U)
Remote device
Low limit (mg/dL)
High limit (mg/dL)
Basal rate (U/Hr)
75
177
0.025
60
105
Android Protected Confirmation
You are going to program
Heart beat 75
Insulin 177U
Basal rate 0.025 U/Hr
Low level 60 mg/dL
High level 105 mg/dL
And more ……
Android Protected Confirmation
You are going to program
Heart beat 75
Insulin 171U
Basal rate 0.025 U/Hr
Low level 62 mg/dL
High level 125 mg/dL
And more ……

## Slide 17: Solution 2: Input Signing
Trusted embedded device
Program
Cancel
Heart beat
Insulin (U)
Remote device
Low limit (mg/dL)
High limit (mg/dL)
Basal rate (U/Hr)
75
177
0.025
60
105
Heart beat 75
Insulin 177U
Basal rate 0.025 U/Hr
Low level 60 mg/dL
High level 105 mg/dL
Notes: Add attacker in the host

## Slide 18: Display manipulation attack
17
177
177
177
7
1777
User sees 177
Device records 1777
Host sends 1777
Insulin
Insulin

## Slide 19: Observation 1
The lack of output integrity – the render of user inputs on the screen – compromises input integrity.

## Slide 20: Solution 3: Overlay
Program
Cancel
Heart beat
Insulin (U)
Remote device
Low limit (mg/dL)
High limit (mg/dL)
Basal rate (U/Hr)
75
177
0.025
60
105
Program
Cancel
Heart beat
Insulin (U)
Remote device
Low limit (mg/dL)
High limit (mg/dL)
Basal rate (U/Hr)

## Slide 21: Attack on Overlay: Output Manipulation
Program
Cancel
Heart beat
Insulin (U)
Remote device
Low limit (mg/dL)
High limit (mg/dL)
Basal rate (U/Hr)
Program
Cancel
Insulin (U)
Heart rate
Remote device
Low limit (mg/cc)
High limit (mg/cc)
Basal rate (U/Hr)

## Slide 22: Overlay: Output Manipulation
Program
Cancel
Insulin (U)
Heart rate
Remote device
Low limit (mg/cc)
High limit (mg/cc)
Basal rate (U/Hr)
75
177
0.025
0.6
1.05
Program
Cancel
75
Heart rate
177
Insulin (U)
Remote device
Low limit (mg/dL)
High limit (mg/dL)
0.025
Basal rate (U/Hr)
60
105
Notes: `Fix unit

## Slide 23: Observation 2
If the protected output is provided out-of-context,
users are more likely not to verify it.
Therefore input integrity can be violated.

## Slide 24: Overlay: Early Form Submission Attack
Textbox in focus
Program
Cancel
Heart beat
Insulin (U)
Remote device
Low limit (mg/dL)
High limit (mg/dL)
Basal rate (U/Hr)
75
17
0.025
60
105
OS triggers click
Fidelius
Trusted overlay from FPGA

## Slide 25: Observation 3
If not all the modalities of inputs are secured simultaneously,
none of them can be fully secured.

## Slide 26: Requirements
Inter-dependency between Input and output
The lack of output integrity – the render of user inputs on the screen – compromises input integrity.

## Slide 27: Requirements
All modalities of input
If not all the modalities of inputs are secured simultaneously, none of them can be fully secured.
Notes: Mention that there is a proof, we keep it simple here

## Slide 28: Requirements
Low cognitive load
If the protected output is provided out-of-context, users are more likely not to verify it. Therefore input integrity can be violated.

## Slide 29: Requirements
Low TCB and easy deploy

## Slide 30: Requirements

## Slide 31: ProtectIOn
Input modalities
Low TCB + fast deployment
IOHub
Notes: orientation

## Slide 32: IO Integrity – Server-side Annotation
Program
Cancel
Heart beat
Insulin (U)
Remote device
Low limit (mg/dL)
High limit (mg/dL)
Basal rate (U/Hr)
<form action="/some_action", signature = "0x45AB…", id = "0x0ab..">
Simultaneous IO
<label for="insulin" secure="true">Insulin (U)</label> <input type="text" id="insulin" name="insulin" secure="true">
ProtectIOn JS

## Slide 33: IO Integrity – HTML Specification
Simultaneous IO
<form action="/some_action", signature = "0x45AB…", id = "0x0ab..">
<label for="insulin" secure="true">Insulin
(U)</label> <input type="text" id="insulin"
name="insulin" secure="true"> …
</form>
ProtectIOn JS
{
"formId": "form1",
"formName": "configure device",
"domain": "secure_site.io",
"size": "400*400",
"SAS": "5:LB",
"ui": [{
"id": "Insulin", "type": "textbox",
"label": “Insulin (U)",
"text":"",
"RE":(0-9)+},
{"id": "Heart rate",
…},
{"id":"b1",
"type": "button",
"label": "Program",
"trigger": "true"},
…],
"signature": "0x45AB...",
"id": "0x0ab.."}
form1.bmp

## Slide 34: IO Integrity – UI QR Code
Simultaneous IO
…
<form action="/some_action", signature = "0x45AB…", id = "0x0ab..">
<label for="insulin" secure="true">
Insulin(U)</label> <input type="text" id="insulin"
name="insulin" secure="true">
…
</form>
…
ProtectIOn JS
…
<img src=“form1.bmp”>
…

## Slide 35: IO Integrity – QR Code Overlay Generation
Simultaneous IO
{
"formId": "form1",
"formName": "configure device",
"domain": "secure_site.io",
"size": "400*400",
"SAS": "5:LB",
"ui": [{
"id": "Insulin", "type": "textbox",
"label": “Insulin (U)",
"text":"",
"RE":(0-9)+},
{"id": "Heart rate",
…},
{"id":"b1",
"type": "button",
"label": "Program",
"trigger": "true"},
…],
"signature": "0x45AB...",
"id": "0x0ab.."}

## Slide 36: IO Integrity – QR Code Overlay Generation
Program
Cancel
Insulin (U)
Heart rate
Remote device
Low limit (mg/cc)
High limit (mg/cc)
Basal rate (U/Hr)
Verified UI from secure_site.io
Simultaneous IO

## Slide 37: IO Integrity – Input
Program
Cancel
Insulin (U)
Heart rate
Remote device
Low limit (mg/cc)
High limit (mg/cc)
Basal rate (U/Hr)
Verified UI from secure_site.io
75
177
0.025
60
105
Simultaneous IO
ProtectIOn JS

## Slide 38: User Attention for Integrity
Untrusted UI
Put 1 in front of all inputs
Trusted UI Overlay
Critical value:
Submit
Cancel

## Slide 39: User Attention: Rethinking Security Indicators for Trusted Path
S&P 2007
CHI 2008
SOUPS 2016
Notes: However the main challenge of designing a robust trusted path solution turned out to be how to focus user attention. Note that the user interaction with the UIs involves a lot of user attention. For trusted path, specifically for our overlay based design, its how to guide users to distinguish between the trusted part and the untrusted part of the screen. A majority of the existing research mostly avoided this crucial discussion and most of them relied on standard security indicates. Such as an icon on the screen or flashing some external LED lights. However, as some existing research pointed out that in the wild, the security indicators does not provide useful security due to the user habituation.

## Slide 40: User Attention for Integrity
Untrusted UI
Put 1 in front of all inputs
Trusted UI Overlay
Critical value:
Submit
Cancel
Notes: We wanted to integrate this attention grabbing mechanism integrated as the part of the UI that is impossible for the user to ignore. And this idea is not completely wild. Similar mechanism are proposed in 2008 as the part of the W3C security standard to fight against click jacking attack. The problem there was to distinguish between the attacker-controlled JS generated button and a button provided by the browser.

## Slide 41: User Attention for Integrity
Untrusted UI
Put 1 in front of all inputs
Trusted UI Overlay
Critical value:
Submit
Cancel

## Slide 42: User Attention for Integrity
Untrusted UI
Put 1 in front of all inputs
Trusted UI Overlay
Critical value:
Submit
Cancel

## Slide 43: User Attention for Integrity
Untrusted UI
Put 1 in front of all inputs
Trusted UI Overlay
Critical value:
Submit
Cancel

## Slide 44: Grabbing User Attention
Output Integrity: Low cognitive load
Several existing mechanisms
Put 1 in front of all inputs
Low cognitive load

## Slide 45: Grabbing User Attention
Put 1 in front of all inputs
Low cognitive load
Output Integrity: Low cognitive load
Several existing mechanisms
  Lightbox

## Slide 46: Grabbing User Attention
Output Integrity: Low cognitive load
Several existing mechanisms
  Lightbox
  Highlight
Low cognitive load
Put 1 in front of all inputs

## Slide 47: Grabbing User Attention
Output Integrity: Low cognitive load
Several existing mechanisms
  Lightbox
  Highlight
  Freezing
Put 1 in front of all inputs
Low cognitive load

## Slide 48: Grabbing User Attention
Put 1 in front of all inputs
Output Integrity: Low cognitive load
Several existing mechanisms
  Lightbox
  Highlight
  Freezing
  Combination
Low cognitive load

## Slide 49: Grabbing User Attention
Output Integrity: Low cognitive load
Several existing mechanisms
  Lightbox
  Highlight
  Freezing
  Combination
How to determine when to engage?
  Track pointer
  Mouse movement on the overlay
Low cognitive load
Notes: The main idea here is to introduce low cognitive load on the user.

## Slide 50: User Attention for Confidentiality
Untrusted UI
Secret value:
Submit
Cancel
Trusted UI
Secret value:
Submit
Cancel

## Slide 51: User Attention for Confidentiality
Untrusted UI
Secret value:
Submit
Cancel

## Slide 52: User Attention for Confidentiality
Differs from the integrity problem
Has to be triggered by the user
  Otherwise the attacker can fake the process
  Outside the control of the attacker
Secure attention sequence (SAS)
  Well-known mechanism
  Ctrl + Alt + Delete
  Intercepted by the IOHub first

## Slide 53: Prototype and TCB
25.16M
20.92M
2M
71K
600K
36.68M
1.9K
3.5K
893
121K
Low TCB
Fast deployment

## Slide 54: Performance
Display latency: 21.67 ms
  ~46 fps
Mouse latency: 250
Keyboard latency: 170
Pointer detection accuracy: 0.997

## Slide 55: What do we learn?
Trusted path is an intractable problem
  System and human interaction
Fairly crowded space
  Fundamentals (simultaneous IO, input modalities…) are overlooked
  Attacks on existing systems
Fundamental security properties
Human perception
  Different mechanisms for Integrity, and confidentiality
How to build more systems around it

## Slide 56
Thank you!

## Slide 57: How to Build a Trusted Path
Server sends messages : HTML, JS …
All modalities of inputs
Host (browser, GPU render, etc.) transforms:
Host is attacker-controlled
Output integrity Users need to report back

## Slide 58: Definition: Violation of Input/output Integrity
Sever sends
Server knows
Given , correct input is
Host sends Output integrity
User sends Input integrity

## Slide 59: Verification
Anything missing in the chain IO integrity violation

## Slide 60: Other contributions
Fast off-chain payments
  Snappy (NDSS 2020)
Anonymous communication
  CoverUp (NSDI 2019)
Monitoring of type-state properties
  Metis (RV 2018)
Rollback protection for SGX
  ROTE (USENIX 2017)

## Slide 61: Attacks
Images are from wired, csmonitor, heimdalsecurity

## Slide 62: Attacks
Images are from wired, csmonitor, heimdalsecurity

## Slide 63: Attacks
Images are from wired, csmonitor, heimdalsecurity

## Slide 64: Attacks
Images are from wired, csmonitor, heimdalsecurity

## Slide 65: Attacks
Images are from wired, csmonitor, heimdalsecurity